## Slide 1: Introduction to Software Testing (2nd edition) Chapter 7.5 Graph Coverage for Specifications
Paul Ammann & Jeff Offutt
http://www.cs.gmu.edu/~offutt/softwaretest/

## Slide 2: Design Specifications
A design specification describes aspects of what behavior software should exhibit
A design specification may or may not reflect the implementation
  More accurately – the implementation may not exactly reflect the spec
  Design specifications are often called models of the software
Two types of descriptions are used in this chapter
  Sequencing constraints on class methods
  State behavior descriptions of software

## Slide 3: Sequencing Constraints
Sequencing constraints are rules that impose constraints on the order in which methods may be called
They can be encoded as preconditions or other specifications
Section 7.4 said that classes often have methods that do not call each other
Class stack
public void push (Object o)
public Object pop ( )
public boolean isEmpty ( )
pop
push
isEmpty
? ? ?
Tests can be created for these classes as sequences of method calls
Sequencing constraints give an easy and effective way to choose which sequences to use

## Slide 4: Sequencing Constraints Overview
Sequencing constraints might be
  Expressed explicitly
  Expressed implicitly
  Not expressed at all
Testers should derive them if they do not exist
  Look at existing design documents
  Look at requirements documents
  Ask the developers
  Last choice : Look at the implementation
If they don’t exist, expect to find more faults !
Share with designers before designing tests
Sequencing constraints do not capture all behavior

## Slide 5: Queue Example
Sequencing constraints are implicitly embedded in the pre and postconditions
  enQueue () must be called before deQueue ()
Does not include the requirement that we must have at least as many enQueue () calls as deQueue () calls
  Can be handled by state behavior techniques
public int deQueue() { // Pre: At least one element must be on the queue. … …
public enQueue (int e) { // Post: e is on the end of the queue.

## Slide 6: File ADT Example
class FileADT has three methods:
open (String fName) // Opens file with name fName
close () // Closes the file and makes it unavailable
write (String textLine) // Writes a line of text to the file
Valid sequencing constraints on FileADT:
An open (f) must be executed before every write (t)
An open (f) must be executed before every close ()
A write (f) may not be executed after a close () unless there is an open (f) in between
A write (t) should be executed before every close ()
1
2
3
4
5
6
open (f)
write(t)
write (t)
close ()
Client that uses FileADT

## Slide 7: Static Checking
Is there a path to a write() that does not go through an open() ?
Is there a path to a close() that does not go through an open() ?
Is there a path from a close() to a write()?
Is there a path from an open() to a close() that does not go through a write() ? (“write-clear” path)
1
2
3
4
5
6
open (f)
write(t)
write (t)
close ()
Is there a path that violates any of the sequencing constraints ?
[ 1, 3, 4, 6 ] – ADT use anomaly!

## Slide 8: Static Checking
close ()
1
2
3
4
5
8
open (f)
write (t)
write (t)
6
7
close ()
Consider the following graph :
[ 7, 3, 4 ] – close () before write () !

## Slide 9: Generating Test Requirements
Use the sequencing constraints to generate test requirements
The goal is to violate every sequencing constraint
1
2
3
4
5
6
open (f)
write (t)
write (t)
close ()
[ 1, 3, 4, 6 ] – ADT use anomaly!
But it is possible that the logic of the program does not allow the pair of edges [1, 3, 4]
That is – the loop body must be taken at least once
Determining this is undecidable – so static methods are not enough

## Slide 10: Test Requirements for FileADT
Cover every path from the start node to every node that contains a write() such that the path does not go through a node containing an open()
Cover every path from the start node to every node that contains a close() such that the path does not go through a node containing an open()
Cover every path from every node that contains a close() to every node that contains a write()
Cover every path from every node that contains an open() to every node that contains a close() such that the path does not go through a node containing a write()
Apply to all programs that use FileADT
If program is correct, all test requirements will be infeasible
Any tests created will almost definitely find faults

## Slide 11: Testing State Behavior
A finite state machine (FSM) is a graph that describes how software variables are modified during execution
Nodes : States, representing sets of values for key variables
Edges : Transitions, possible changes in the state
Off
On
switch up
switch down

## Slide 12: Finite State Machine—Two Variables
Tropical Depression
circulation = yes
windspeed < 39mph
Tropical Storm
circulation = yes
windspeed = 39..73 mph
Major Hurricane
circulation = yes
windspeed >= 110 mph
Hurricane
circulation = yes
windspeed 74..109 mph
Something Else
circulation = no
Other variables may exist but not be part of state

## Slide 13: Finite State Machines are Common
FSMs can accurately model many kinds of software
  Embedded and control software (think electronic gadgets)
  Abstract data types
  Compilers and operating systems
  Web applications
Creating FSMs can help find software problems
Numerous languages for expressing FSMs
  UML statecharts
  Automata
  State tables (SCR)
  Petri nets
Limitation : FSMs are not always practical for programs that have lots of states (for example, GUIs)

## Slide 14: Annotations on FSMs
FSMs can be annotated with different types of actions
  Actions on transitions
  Entry actions to nodes
  Exit actions on nodes
Actions can express changes to variables or conditions on variables
These slides use the basics:
  Preconditions (guards) : conditions that must be true for transitions to be taken
  Triggering events : changes to variables that cause transitions to be taken
This is close to the UML Statecharts, but not exactly the same

## Slide 15: Example Annotations
Closed
Open
open elevator door
pre: elevSpeed = 0
trigger: openButton = pressed

## Slide 16: Covering FSMs
Node coverage : execute every state (state coverage)
Edge coverage : execute every transition (transition coverage)
Edge-pair coverage : execute every pair of transitions (transition-pair)
Data flow:
  Nodes often do not include defs or uses of variables
  Defs of variables in triggers are used immediately (the next state)
  Defs and uses are usually computed for guards, or states are extended
  FSMs typically only model a subset of the variables
Generating FSMs is often harder than covering them …

## Slide 17: Deriving FSMs
With some projects, an FSM (such as a statechart) was created during design
  Tester should check to see if the FSM is still current with respect to the implementation
If not, it is very helpful for the tester to derive the FSM
Strategies for deriving FSMs from a program:
  Combining control flow graphs (wrong)
  Using the software structure (wrong)
  Modeling state variables
Example based on a digital watch …
  Class Watch uses class Time

## Slide 18: Class Watch
class Watch
// Constant values for the button (inputs)
private static final int NEXT = 0;
private static final int UP = 1;
private static final int DOWN = 2;
// Constant values for the state
private static final int TIME = 5;
private static final int STOPWATCH = 6;
private static final int ALARM = 7;
// Primary state variable
private int mode = TIME;
// Three separate times, one for each state
private Time watch, stopwatch, alarm;
public Watch () // Constructor
public void doTransition (int button) // Handles inputs
public String toString () // Converts values
class Time ( inner class )
private int hour = 0;
private int minute = 0;
public void changeTime (int button)
public String toString ()

## Slide 19
// Takes the appropriate transition when a button is pushed.
public void doTransition (int button)
{
switch ( mode )
{
case TIME:
if (button == NEXT)
mode = STOPWATCH;
else
watch.changeTime (button);
break;
case STOPWATCH:
if (button == NEXT)
mode = ALARM;
else
stopwatch.changeTime (button);
break;
case ALARM:
if (button == NEXT)
mode = TIME;
else
alarm.changeTime (button);
break;
default:
break;
}
} // end doTransition()
// Increases or decreases the time.
// Rolls around when necessary.
public void changeTime (int button)
{
if (button == UP)
{
minute += 1;
if (minute >= 60)
{
minute = 0;
hour += 1;
if (hour > 12)
hour = 1;
}
}
else if (button == DOWN)
{
minute -= 1;
if (minute < 0)
{
minute = 59;
hour -= 1;
if (hour <= 0)
hour = 12;
}
}
} // end changeTime()

## Slide 20: 1. Combining Control Flow Graphs
The first instinct for inexperienced developers is to draw CFGs and link them together
This is really not an FSM
Several problems
  Methods must return to correct callsites—implicit nondeterminism
  Implementation must be available before graph can be built
  This graph does not scale up
Watch example …

## Slide 21: CFGs for Watch
5
6
7
8
1
2
3
4
11
12
13
9
10
14
doTransition ()
1
12
6
8
2
4
10
7
9
3
5
11
changeTime ()

## Slide 22: 2. Using the Software Structure
A more experienced programmer may map methods to states
These are really not states
Problems
  Subjective—different testers get different graphs
  Requires in-depth knowledge of implementation
  Detailed design must be present
Watch example …

## Slide 23: Software Structure for Watch
button
inMain
inChangeTime
inDoTransition
button==NEXT / change mode
button==UP or button==DOWN
button==DOWN / change hour, minute
button==UP / change hour, minute
??? Not clear what triggers this …
??? Should inChangeTime transit back to inMain???

## Slide 24: 3. Modeling State Variables
More mechanical
State variables are usually defined early
First identify all state variables, then choose which are relevant
In theory, every combination of values for the state variables defines a different state
In practice, we must identify ranges, or sets of values, that are all in one state
Some states may not be feasible
Notes: These next few slides do not match the book (edition 2), but we think it’s a better model.

## Slide 25: State Variables in Watch
Constants
NEXT, UP, DOWN
TIME, STOPWATCH, ALARM
Non-constant variables in class Watch
int mode (values: TIME, STOPWATCH, ALARM)
Time watch, stopwatch, alarm
Not relevant, really just values

## Slide 26: State Variables in Time
Non-constant variables in class Time
int hour (values: 1..12)
int minute (values: 0 .. 59)
12 X 60 values is 720 states
Clearly, that is too many
Combine values into ranges of similar values :
hour : 1.. 11, 12
minute : 0, 1.. 59
Four states : (1..11, 0); (12, 0); (1..11, 1.. 59); (12, 1 .. 59)
Clumsy ... Not sequential …
let’s combine hour and minute …
Time : 12:00, 12:01..12:59, 01:00 .. 11:59
These require lots of thought and semantic domain knowledge of the program

## Slide 27: Hierarchical FSMs
One FSM is contained within the other
S1
S3
S2
a
b
c
Class Watch uses class Time
How can we model two classes—one that uses another?

## Slide 28: Watch / Time Hierarchical FSM
next
next
next
mode = TIME
h : m =
12:00
h : m =
12:01 .. 12:59
h : m =
1:00 .. 11:59
up
down
up
down
up
up
up
down
down
down
mode = STOPWATCH
h : m =
12:00
h : m =
12:01 .. 12:59
h : m =
1:00 .. 11:59
up
down
up
down
up
up
up
down
down
down
mode = ALARM
h : m =
12:00
h : m =
12:01 .. 12:59
h : m =
1:00 .. 11:59
up
down
up
down
up
up
up
down
down
down
Notes: This differs from the book to give students two views of the same problem. Hierarchical FSMs are slightly more advanced, but probably more elegant for modeling this example.

## Slide 29: Summary–Tradeoffs in Applying Graph Coverage Criteria to FSMs
Two advantages
  Tests can be designed before implementation
  Analyzing FSMs is much easier than analyzing source
Three disadvantages
  Some implementation decisions are not modeled in the FSM
  There is some variation in the results because of the subjective nature of deriving FSMs
  Tests have to be “mapped” to actual inputs to the program – the names that appear in the FSM may not be the same as the names in the program